## Slide 1
بسم الله الرحمن الرحيم

## Slide 2: Minor Connectors

## Slide 3: Minor Connectors
Connects components to the major connector
Direct retainer
Indirect retainer
Rest

## Slide 4: Requirements of minor connector:
1.sufficient rigidity . Like the major connector, the minor connector must have sufficient bulk to be rigid to transmit forces between the linked components.

## Slide 5: 2. must not impinge on marginal gingival tissues. Slight relief is required when crossing the gingival margin especially in tooth-mucosa borne dentures.

## Slide 6: 3.Minor connectors should be located at least 5mm from other vertical components.

## Slide 7: Functions of Minor Connectors
1. Unification and rigidity
2. Stress distribution
3. Bracing through contact with guiding planes
4. Maintain a path of insertion

## Slide 8: Types of Minor Connectors
Embrasure Minor Connectors
Between two adjacent teeth

## Slide 9: Embrasure Minor Connectors
Triangular shaped in cross section
Joins major connector at right angles
Relief placed so connector not directly on soft tissue

## Slide 10: Proximal minor connector: Those that join the clasp assembly to the major connector. If the minor connector is located on a proximal surface of a tooth adjacent to edentulous areas, it should be broad buccolingually to provide strength but thin mesiodistally to minimize encroachment on the saddle area.

## Slide 11
mesial and distal minor connectors and proximal plates adjacent to the edentulous areas should swing back to join the major connector in a rounded acute angle in order to increase gingival exposure.

## Slide 12: Gridwork minor connectors that connect the denture base and teeth to the major connector.
Latticework construction,
Mesh construction,
Bead, wire, or nail-head minor connectors .

## Slide 13: Gridwork Minor Connectors
Open lattice work
mesh types

## Slide 14: Mesh type
Flatter
Potentially more rigid
Less retention for acrylic if openings are small

## Slide 15: Lattice Type
Potentially superior retention
Interferes with setting of teeth, if struts are too thick
This type can be relined easily after ridge resorption.

## Slide 16: Bead, wire, or nail-head minor connectors
no relief is provided for this type of minor connector.
It cannot be relined if ridge resorption takes place. It should be used on tooth-supported ridges.

## Slide 17: Gridwork Relief
Usually one thickness of baseplate wax is about
1 mm of relief sufficient
the space provided by the relief wax is available for the mechanical retention of the acrylic resin

## Slide 18
The minor connector for the mandibular distal extension base should extend posteriorly about two-thirds the length of the edentulous ridge and should have elements on both lingual and buccal surfaces.

## Slide 19: Mandibular Gridwork Design

## Slide 20
Minor connectors for maxillary distal extension denture bases should extend the entire length of the residual ridge and should be of a ladderlike and loop design.

## Slide 21
Those that serve as an approach arm for a vertical projection or bar-type clasp.

## Slide 22: Finishing Lines
The junction of gridworks to the major connector should be in the form of a butt joint with a slight undercut in the metal. The angle formed by the metal at this juncture must not be greater than 90 degrees.

## Slide 23
If these butt joints occur on the outer aspect of the major connector they are called external finish lines; if they are on the internal or tissue side of the major connector ,they are internal finish lines .

## Slide 24: Angle the finish line forms with major connector – less than 90 degree.

## Slide 25: Finish line located too far medially– natural contour of palate altered by thickness of acrylic Too far buccally– difficult to create a natural contour of acrylic resin on lingual surface of artificial teeth

## Slide 26: 90-degree butt-type joints

## Slide 27
Tissue stop : a small projection of metal at the distal end of an extension base frame that contacts the cast and prevents downward movement of the plastic retention area during packing with resin

## Slide 28: Closure of the flask under hydraulic pressure can causes distortion of the framework, pushing it tissue ward.

## Slide 32
THANK YOU